## Slide 1: Enhancing the Variable Infiltration Capacity Model to Account for Natural and Anthropogenic Impacts on Evapotranspiration in the North American Monsoon Region
Theodore J. Bohn and Enrique R. Vivoni, Arizona State University
NLDAS Monthly Telecon, Feb 17, 2016

## Slide 2: Importance of Accurate ET in Land Surface Models
2nd largest term in terrestrial water budget
  Arid regions: ET ≈90% of P
Least-constrained by observations
Errors in ET cause errors in Q ( ≈ P – ET)
Errors impact estimates of ET-P feedbacks
Trenberth et al. (2007)

## Slide 3: North American Monsoon (NAM)
Gulf of
Mexico
Pacific
Ocean
Surge
Tropical Moisture
P
ET
Summer monsoon provides >50% of annual rainfall here
40% P-recycling
Monsoon highly variable
LSMs disagree on ET here
Could better ET improve forecasts?

## Slide 4: ET Partitioning
200 m
Open Shrublands
Forests

## Slide 5: Land Cover/Land Use Change
Irrigated Agriculture
Both winter and summer crops
7% of land area
Ignored in large-scale studies
Deforestation / Pasture Clearing
>10,000 km2 in NAM region
Most of it since 1970s

## Slide 6: Science Questions
What are the major sources of ET in the NAM region?
How do they vary in time/space?
What are the major underlying mechanisms?
Bohn, T. J., and E. R. Vivoni, 2016: A Process-Based Characterization of Evapotranspiration Sources in the North American Monsoon Region, WRR, 52(1), 358-384, doi: 10.1002/2015WR017934.

## Slide 7: VIC Land Surface Model
VIC 4.2
Large-scale hydrology model (Liang et al., 1994)
1/16 degree spatial resolution
Hourly time step
Solves moisture and energy balances
Mosaic of land cover “tiles”
Calibrated over Mexico by Zhu et al. (2007)
Liang, X., et al., 1994: A simple, hydrologically based model of land surface water and energy fluxes for GSMs, J. Geophys. Res., 99(D7), 14415-14428.
Zhu, C., et al., 2007: Role of antecedent land surface conditions in warm season precipitation over northwestern Mexico, J. Climate, 20, 1774-1791.

## Slide 8: VIC Modifications
Implement clumped vegetation scheme
Allows evaporation from exposed soil between plants
Veg canopy cover fraction fv derived from NDVI
Esoil taken from ARNO model (Francini and Pacciani 1991)
Francini and Pacciani., 1991: Comparative analysis of several conceptual rainfall-runoff models, J. Hydrol., 122, 161-219.
Bohn and Vivoni, WRR (2016)

## Slide 9: VIC Modifications
Read time series of vegetation characteristics (2000-2012) as forcing variables:
  NDVI: MODIS 16-day 500m
  LAI: MODIS 8-day 1000m
  Albedo: MODIS 16-day 500m
Irrigation
  Scheme of Haddeland et al. (2006)
  Crop/Fallow Fraction derived from MODIS reflectances (Lobell and Asner, 2004)
Haddeland, I., et al., 2006: Effects of irrigation on the water and energy balances of the Colorado and Mekong river basins, J. Hydrol., 324(1), 210-223.
Lobell and Asner, 2004: Cropland distributions from temporal unmixing of MODIS data, Rem. Sens. Env., 93(3), 412-422.

## Slide 10: PVI-Crop Area Relationship
Winter
Summer

## Slide 11: Timeseries of Crop Areas
RCO
COM
BCS_S
SON_S
SIN
CHI_NWC
Method reproduces Yaqui Valley shortage in 2004-2005
Areas are expressed as fractions of total MODIS crop pixel area within each region

## Slide 12: Model Validation: Eddy Covariance Towers
BO1
SRM
Irrigation=TRUE
Irrigation=FALSE
Big Leaf
Clumped

## Slide 13: Gridded Meteorological Inputs
Livneh et al (2015)
Met. Station Data covering 1950-2013:
  5000 SMN station observations across Mexico
  20000 COOP stations across USA
Daily Fields:
  Total precipitation
  Max/min air temperatures
  Average wind speed
1/16 degree resolution
Elevation correction
JFM Precip, 2000-2012
JAS Precip, 2000-2012
Livneh, B., et al., 2015: A spatially comprehensive hydrometeorological data set for Mexico, the U.S., and southern Canada 1950-2013, Nature Scientific Data, 2, 150042, doi: 10.1038/sdata.2015.42.

## Slide 14: VIC ET, 2000-2012
Annual
Winter
Summer
Largest fluxes: mountain forests and irrigated agriculture
  22% and 9% of ET by volume

## Slide 15: Comparison with Other Products
Product | Type | Comment
Mu et al (2011) | RS-PM | Exposed soil area related to FPAR
Sheffield et al (2010) | RS-PM | Big Leaf Formulation
North American Regional Reanalysis (NARR) | Coupled land-atmosphere model; assimilates met. | Over Mexico, P has no elevation correction
North American Land Data Assimilation (NLDAS) | Offline LSMs driven by common met. forcings | Over Mexico, P has no elevation correction
VIC 4.0.3 | LSM | Big Leaf Formulation
NOAH | LSM | 
MOSAIC | LSM | 
Remote Sensing – Penman-Monteith (RS-PM)
No soil model
Soil moisture related to air humidity
Process-based models
None of these handle irrigation

## Slide 16: Small Basin ET/P Ratios
ETobs = Pobs – Qobs
Pobs = P used by model
Product | Mean ET/P | Bias
Obs | 0.86 | 0.00
VIC | 0.85 | -0.01
Mu et al 2011 | 0.67 | -0.19
Sheffield et al 2015 | 0.56 | -0.30
NARR | 0.71 | -0.15
NLDAS-VIC | 0.80 | -0.06
NLDAS-NOAH | 0.87 | +0.01
NLDAS-MOSAIC | 0.95 | +0.09

## Slide 17: Other Gridded ET Products, 2000-2012
Mu et al (2011) lacks ET over deserts
Sheffield et al (2010) underestimates ET almost everywhere
NARR and NLDAS
  Discontinuity at US-Mexico border
  Underestimate ET over SMO
All products underestimate ET over croplands

## Slide 18: Annual ET Partitioning
VIC partitioning over whole domain:
  Esoil = 60%
  Transp = 32%
  Ecan = 8%
NLDAS-VIC has zero Esoil almost everywhere (except over pure bare soil pixels)
VIC, NLDAS-NOAH, and NLDAS-MOSAIC agree:
  Shrublands: Esoil = 35-100 %
  Forests: Esoil = 5-35 %

## Slide 19: Seasonal Cycle
Smaller March peak in CAMX and AZNM
Mu et al (2011) lacks summer ET in AZNM
NARR and NLDAS-VIC overestimate late spring ET in AZNM
NLDAS-VIC underestimates winter ET in AZNM
NLDAS-VIC attributes all ET to Transp.
ET peaks in August everywhere except CAMX
CAMX
AZNM
CORE

## Slide 20: Temporal Response of Land Cover
Flux | Annual P | Same Season P |  |  |  | Previous Season P |  |  | 
 |  | JFM | AMJ | JAS | OND | JFM | AMJ | JAS | OND
P | 1.0 | 1.0 | 1.0 | 1.0 | 1.0 | 0.69 | 0.06 | -0.13 | -0.20
ET | 0.90 | 0.96 | 0.88 | 0.93 | 0.92 | 0.72 | 0.47 | 0.05 | 0.10
Esoil | 0.81 | 0.95 | 0.95 | 0.84 | 0.96 | 0.68 | 0.17 | -0.16 | -0.20
T | 0.68 | 0.76 | 0.18 | 0.68 | -0.07 | 0.67 | 0.89 | 0.22 | 0.79
Correlations between Fluxes and Precipitation
Yellow = statistically significant
Esoil controlled by current season’s P
Transpiration controlled by previous season’s P
Crop ET has essentially ZERO correlation with P
Shrublands
Forests

## Slide 21: Conclusions
Model Performance
New VIC performs well at eddy covariance towers
New VIC outperforms most other available products over NAM region
  ET/P
  Irrigated croplands
Mu et al (2011) and Sheffield et al (2010) substantially underestimate ET in the NAM region
  Lack soil moisture model
  Underestimate Esoil

## Slide 22: Conclusions
ET Sources
Mountain forests and irrigated agriculture are strongest sources of ET in the NAM region
22% and 9% of ET by volume
ET Partitioning
Primary ET component = Esoil (60%)
Desert Shrublands = Esoil
Mountain Forests = Transp.
ET-P relationships
Esoil (shrublands) controlled by current season’s P
Transp (forests) controlled by previous season’s P
ET over irrigated croplands is not controlled by P
Implications for P-recycling and forecast skill?

## Slide 23: Future Work
Currently working on incorporating VIC into WRF-Hydro (collaboration with Bart Nijssen at UW)
Examine impacts of land cover/use change on ET-P coupling in NAM region

## Slide 24: Thank You
T. Bohn is supported by Grant 1216037 from the U.S. National Science Foundation (NSF) Science, Engineering and Education for Sustainability (SEES) Post-Doctoral Fellowship program.
This material is based upon work supported by the National Science Foundation under Grant SES-0951366, Decision Center for a Desert City II: Urban Climate Adaptation.
Bohn, T. J., and E. R. Vivoni, 2015: A Process-Based Characterization of Evapotranspiration Sources in the North American Monsoon Region, Water Resources Research (in review).

## Slide 25: Land-Atmosphere Coupling (ET-P)
GLACE - Koster et al. (2004)
Great Plains
North American Monsoon (NAM) Region
Higher-resolution studies: 40% P-recycling in the NAM region (Hu and Dominguez, 2015)

## Slide 26: Moisture Transport in Monsoon
Dominguez et al (2008) analyzed monsoon moisture transport, using NARR + analytical model
Recycling ratios of up to 25%
Dominguez, F., et al., 2008: Precipitation recycling variability and ecoclimatological stability – a study using NARR data. Part II: North American Monsoon region, J. Climate, 21, 5187-5203, doi: 10.1175/2008JCLI1760.1.
Precipitation
Moisture Flow Paths

## Slide 27: Performance Statistics
Plant Functional Type (PFT) | N | (mm d-1) | JJA [mm d-1] (%) |  | (mm d-1) | Median NSE
ENF | 8 | -0.1050 | -0.0421 (-2) | 0.7282 | 0.7872 | 0.4947
DBF | 2 | -0.0671 | -0.2151 (-7) | 0.7246 | 1.2126 | 0.6351
WSA | 2 | -0.0125 | -0.1639 (-7) | 0.7828 | 0.8419 | 0.3806
SAV | 1 | 0.1533 | -0.0972 (-10) | 0.7716 | 0.7800 | 0.5651
CSH | 4 | -0.2680 | -0.3641 (-27) | 0.6461 | 0.6610 | 0.1450
OSH | 8 | -0.1115 | -0.1115 (-14) | 0.7397 | 0.6234 | 0.5305
GRA | 21 | -0.0091 | -0.1028 (-10) | 0.7824 | 0.8542 | 0.5331
CRO – Irrigated Maize/Soy | 6 | -0.0062 | 0.0717 (3) | 0.8476 | 0.8022 | 0.6979
CRO – Rainfed Maize/Soy | 1 | 0.0511 | -0.1682 (-6) | 0.5793 | 1.1252 | 0.2911
CRO – Rainfed Wheat | 1 | -0.0400 | 0.1352 (7) | 0.7478 | 0.7500 | 0.4910
CRO – Irrigated Orchard | 1 | 0.2812 | 0.2417 (12) | 0.6870 | 0.6911 | 0.0836
CRO – Irrigated Maize/beans with 35% crop cover | 1 | 0.2533 | 0.3527 (12) | 0.8060 | 0.6999 | 0.5955
Plant Functional Type (PFT) | N |  |  |  |  | Median NSE
ENF | 8 | -0.1050 | -0.0421 (-2) | 0.7282 | 0.7872 | 0.4947
DBF | 2 | -0.0671 | -0.2151 (-7) | 0.7246 | 1.2126 | 0.6351
WSA | 2 | -0.0125 | -0.1639 (-7) | 0.7828 | 0.8419 | 0.3806
SAV | 1 | 0.1533 | -0.0972 (-10) | 0.7716 | 0.7800 | 0.5651
CSH | 4 | -0.2680 | -0.3641 (-27) | 0.6461 | 0.6610 | 0.1450
OSH | 8 | -0.1115 | -0.1115 (-14) | 0.7397 | 0.6234 | 0.5305
GRA | 21 | -0.0091 | -0.1028 (-10) | 0.7824 | 0.8542 | 0.5331
CRO – Irrigated Maize/Soy | 6 | -0.0062 | 0.0717 (3) | 0.8476 | 0.8022 | 0.6979
CRO – Rainfed Maize/Soy | 1 | 0.0511 | -0.1682 (-6) | 0.5793 | 1.1252 | 0.2911
CRO – Rainfed Wheat | 1 | -0.0400 | 0.1352 (7) | 0.7478 | 0.7500 | 0.4910
CRO – Irrigated Orchard | 1 | 0.2812 | 0.2417 (12) | 0.6870 | 0.6911 | 0.0836
CRO – Irrigated Maize/beans with 35% crop cover | 1 | 0.2533 | 0.3527 (12) | 0.8060 | 0.6999 | 0.5955